## Slide 1
This project has been funded with support from the European Commission. This publication reflects the views only of the author, and the Commission cannot be held responsible for any use which may be made of the information contained therein.
Application of water balances for supporting River Basin Management planning
Assis. Prof. Dr. Eng. Emil Tsanov
University of Architecture, Civil Engineering and Geodesy, Sofia, Bulgaria
Theme-based Staff Training in UACEG
Reflection of the water policies in the education: insights form the Bulgarian experience
Sofia/ 29-31.05.2019

## Slide 2: Legislation
Water Framework Directive (WFD) 2000/60/ЕС
  River basins
  Preventive action
  River basin management plans (per 6 years) – include the best combination of measures
  To achieve good status for all water bodies till 2015
  Blueprint to safeguard Europe’s Water Resources
    About half of EU surface waters are unlikely to reach good ecological status in 2015
    Proposing water accounting
  Common implementation strategy
  Water accounting and efficiency objectives at sectorial level
  Guidance Document on the application of water balances for supporting the implementation of the Water Framework Directive (WFD)
  Accounting for future climate change scenarios
  Water balances can also be used as the basis for emergency plans in the case of water shortages
  based on the UN System of Environmental Economic Accounting for Water (SEEA-Water) and its ‘Asset Accounts’
  Based on number of studies- one of them ABOT project
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders

## Slide 3: “Assessment of water Balances and Optimisation based Target setting across EU River Basins (ABOT)”
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Water balance modeling
in 4 pilot River Basins
across Europe:
Tiber (Italy),
Mulde (Germany),
Ali-Efenti Pinios (Greece),
Vit (Bulgaria)

## Slide 4: Vit river sub-basin
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Vit river sub-basin on the map of Bulgaria

## Slide 5: Combine approach
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Step 1: Modeling
WEAP
SEEAWater
Step 2: Mitigation measures
Measures by sector
Indicative curves
Step 3: Multi objective optimization
MatLab
Pareto front
Natural-social circle of water
Water users
Households
Industry
Irrigation
Natural water
Surface
Ground
Sustainable water management
Scenarios
Decision making

## Slide 6: Hydrological data
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Chart: Month
Търнене | 32.946 | 37.951 | 49.241 | 64.939 | 65.554 | 40.793 | 33.607 | 30.887 | 18.624 | 20.242 | 21.458 | 28.554
Average monthly river flow at Tarnene station for the period 2000 – 2009 г. (NIMH)
Chart: 
Плевен | 37.9 | 35.3 | 42.8 | 52.1 | 53.5 | 57.7 | 70.9 | 62.8 | 67.3 | 46.24 | 30.87 | 43.29
Тетевен | 41.1 | 36.8889 | 48.3 | 64.2 | 124.5 | 108.7 | 93.7 | 83.7 | 88.9 | 46.83 | 40.16 | 42.53
Average monthly precipitation for the period 2000 - 2009 г. (NIMH)
Chart: Year
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009
Плевен | 395 | 562 | 868 | 564 | 509 | 947 | 490 | 585 | 468 | 619
Тетевен | 509 | 765 | 1030 | 658 | 692 | 1219 | 756 | 1037 | 752 | 740.2
Annual precipitation for the period 2000 – 2009 г. (NIMH)

## Slide 7: Hydrological data
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Chart: Month
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Плевен | 32.8 | 27.2 | 25.7 | 28.2 | 79.8 | 33.6 | 99.4 | 41.3 | 0 | 50.4 | 0.4 | 28.6
Тетевен | 32 | 8 | 38 | 65 | 135 | 121 | 129 | 99 | 8 | 109 | 1 | 39
Monthly precipitation for 2011 (NIMH)
Chart: Month
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12
Плевен | 40 | 98 | 40 | 22 | 32 | 59 | 102 | 35 | 60 | 56 | 11 | 64
Тетевен | 62 | 50 | 52 | 36 | 57 | 140 | 127 | 54 | 72 | 32.3 | 12.6 | 45.3
Monthly precipitation for 2009 (NIMH)

## Slide 8: Evaluation of input information
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Histogram and theoretical curve of normal distribution- accounted water
Normal Q-Q plot – accounted water
Main statistic parameters
Detrended normal Q-Q plot
Average |  | 99.0474
95% confidence interval | Lower boundary | 91.5616
 | Upper boundary | 106.5331
Median |  | 98.2000
Standard variation |  | 32.75906
Min |  | 19.20
Max |  | 180.40
Range |  | 161.20
skewness |  | 0.007
kurtosis |  | -0.128
Distribution is normal with value of the null hypothesis Sig(P)=0.995!

## Slide 9: Settlements
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Population in Vit river sub-basin (own processing of database from NSI)
General information on supplied and accounted water in Vit river sub-basin (own processing of database from NSI)
Chart: Population
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009
Population-Vit Basin | 230125 | 226913 | 223174 | 220893 | 215944 | 214783 | 211835 | 212029 | 210434 | 208483
Population in villages | 77368 | 73345 | 72126 | 72759 | 69610 | 70413 | 69952 | 69441 | 68277 | 67597
Population in towns | 152757 | 153568 | 151048 | 148134 | 146334 | 144370 | 141883 | 142588 | 142157 | 140886
Chart: Year
| 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009
Supplied water | 26056276 | 24138716 | 21679655 | 21893432 | 20242142 | 23399738 | 24639032 | 23530176 | 23327524 | 19394120
Accounted water | 13383291 | 11926039 | 10886264 | 11492645 | 11057010.026 | 10985333.011 | 10169186.994 | 10072898.688 | 9824691.76 | 9360423.846

## Slide 10: Modelling
WEAP-Water evaluation and planning
It solves a wide range of problems
It can be applied at the river basin level, several river basins as well as the lower level
Appropriate for analyzing various scenarios of what-if type
Adaptive to farming practices
Suitable for detailed modeling of water demand
WEAP can work as COM Automation Server
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders

## Slide 11: Developing the model structure
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Modeling scheme of Vit river sub-basin
15 sub catchments;
104 design nodes:
  77 simulating settlements, of which 47 in Pleven WO and 30 Lovetch WO;
  15 simulating private and public water user using ground water by drills води.
  12 for reservoir management, for PH, industry, WWTP and pumping stations.
5 reservoirs with economic significance
8 simulating ground water bodies
3 controlling minimal river runoff
1 other type water supplier
1 for hydrometric stations at Tarnene

## Slide 12: Modelling of settlements
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Input data
Population
Average water use
Water losses (non-revenue water)
Coefficient of monthly variation
Water balance
Settlement

## Slide 13: Modelling of sub-catchments
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Input data
Rainfall Runoff method
Area
Irrigated and non irrigated areas
Crops
Crop coefficient
Effective precipitation
Precipitation
Irrigation efficiency
Evapotranspiration
Water balance
Sub-catchment

## Slide 14: Modelling of reservoirs
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Input data
Inflow
Total volume
Initial volume
Key curve
Transpiration
Water losses to GWB
Volume
Technical specifications- working volume, dead volume and others.
Reservoir
Water balance

## Slide 15: Results
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
(flow rates at Tarnene HMS)
2009 for calibrating
Annual difference of +2.1%
2011 for validating
Annual difference of -1.77%
Red- observed flow rate
Blue- simulated flow rate

## Slide 16: Results
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
(stored water volumes in reservoirs in 2009)
Gorni dabnik reservoir- annual diff.of -5.93%
Sopot reservoir- annual diff. of -0.45%
Red- observed flow rate
Blue- simulated flow rate
Telish reservoir- annual diff. of +0.45%

## Slide 17: SEEA-Water
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Flows from
the environment
to the economy
Inland water resource system and other resources
of which: ISIC div. 36 - Collection, purification and distribution of water
Exports
Households
ISIC 37 – канализация
Industries
ISIC
Imports
Flows within
the economy
Flows from the economy into the
environment
Inland water resource system and other sources

## Slide 18: Application of SEEA-Water
INDUSTRY
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
TELISH RESERVOIR
GORNI DABNIK
RESERVOIR
DOLNI DABNIL
RESERVOIR
GROUND WATER
PUBLIC WATER SUPPLY
SETTLEMENTS
HOUSHOLDS/PUBLIC
IMPORTED WATER (from
other river basin)
IRRIGATION
IRRIGATION
IRRIGATION
Abstraction from nature
Within economy
Return water
Within nature
VIT RIVER
HPP RAKITA
INDUSTRY
HPP GORNI DABNIK
SEWERAGE
HPP TELISH

## Slide 19
 |  |  |  |  |  |  |  | units: million m3 |  |  |  | 
 |  | Industries (by ISIC category) |  |  |  |  |  |  |  | Households | Rest of the world | Total
 |  |  | 5-33, |  |  |  |  | 38,39, |  |  |  | 
 |  | 1-3 | 41-43 | 35 | 36 |  | 37 | 45-99 | Total |  |  | 
From the environment | 1. Total abstraction(=1.a+1.b = 1.i+1.ii) | 12.66 | 6.02 | 63.87 | 73.40 |  | 0 | 0 | 155.24 | 0.24 |  | 155.49
 | 1.a. Abstraction for own use | 12.66 | 6.02 | 63.87 |  |  |  |  | 81.84 | 0 |  | 81.84
 | 1.b. Abstraction for distribution |  | 0 | 0 | 73.40 |  |  |  | 73.40 | 0 |  | 73.40
 | 1.i. From inland water resources: | 12.66 | 6.02 | 63.87 | 73.40 |  | 0 | 0 | 155.24 | 0.24 |  | 155.49
 | 1.i.1 Surface water | 0 |  | 63.87 | 66.32 |  | 0 |  | 130.19 | 0 |  | 130.19
 | From Vit river to HPP Rakita |  |  |  | 50.39 |  |  |  |  |  |  | 
 | -from reservoirs to industry |  |  |  | 2.65 |  |  |  |  |  |  | 
 | -from reservoirs to irrigation |  |  |  | 13.28 |  |  |  |  |  |  | 
 | -from reservoirs to HPPs |  |  | 63.87 |  |  |  |  |  |  |  | 
 | 1.i.2 Groundwater | 0.00 | 6.02 | 0.00 | 7.08 |  | 0 | 0 | 13.10 | 0 |  | 13.10
 | For public water supply |  |  |  | 7.08 |  |  |  |  | 0.24 |  | 
 | For industry |  | 6.02 |  |  |  |  |  |  |  |  | 
 | 1.i.3 Soil water | 12.25 | 0 | 0 | 0 |  |  | 0 | 12.25 | 0 |  | 12.25
 | 1.ii. From others: | 0 | 0 | 0 | 0 |  | 0 | 0 | 0.00 |  |  | 0.00
 | 1.ii.1 Collection of precipitation | 0 | 0 | 0 | 0 |  | 0 | 0 | 0.00 | 0 |  | 
 | 1.ii.2 Abstraction from the sea | 0 | 0 | 0 | 0 |  | 0 | 0 | 0.00 | 0 |  | 
Within the economy | 2. Use of water received from other economic units | 8.65 | 2.23 | 32.32 | 12.30 |  | 9.99 | 2.39 | 67.56 | 7.00 | 0 | 74.55
 | 2.а. Reused water |  |  |  |  |  |  |  |  |  |  | 
 | 2.b. Wastewater to sewerage |  |  |  |  |  |  |  |  |  |  | 
3. Total use of water (=1+2) |  | 20.90 | 8.25 | 96.19 | 85.70 |  | 9.99 | 2.39 | 223.5 | 7.24 | 0 | 230.34
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Physical use table (according to the model in SEEA-Water)

## Slide 20
 |  |  |  |  |  |  |  | units: million m3 |  |  |  | 
 |  | Industries (by ISIC category) |  |  |  |  |  |  |  | Households | Rest of the world | Total
 |  |  | 5-33, |  |  |  |  | 38,39, |  |  |  | 
 |  | 1-3 | 41-43 | 35 | 36 |  | 37 | 45-99 | Total |  |  | 
From the environment | 1. Total abstraction (=1.a+1.b = 1.i+1.ii) | 12.66 | 6.02 | 63.87 | 73.40 |  | 0 | 0 | 155.24 | 0.24 |  | 155.49
 | 1.a. Abstraction for own use | 12.66 | 6.02 | 63.87 |  |  |  |  | 81.84 | 0 |  | 81.84
 | 1.b. Abstraction for distribution |  | 0 | 0 | 73.40 |  |  |  | 73.40 | 0 |  | 73.40
 | 1.i. From inland water resources: | 12.66 | 6.02 | 63.87 | 73.40 |  | 0 | 0 | 155.24 | 0.24 |  | 155.49
 | 1.i.1 Surface water | 0 |  | 63.87 | 66.32 |  | 0 |  | 130.19 | 0 |  | 130.19
 | From Vit river to HPP Rakita |  |  |  | 50.39 |  |  |  |  |  |  | 
 | -from reservoirs to industry |  |  |  | 2.65 |  |  |  |  |  |  | 
 | -from reservoirs to irrigation |  |  |  | 13.28 |  |  |  |  |  |  | 
 | -from reservoirs to HPPs |  |  | 63.87 |  |  |  |  |  |  |  | 
 | 1.i.2 Groundwater | 0.00 | 6.02 | 0.00 | 7.08 |  | 0 | 0 | 13.10 | 0 |  | 13.10
 | For public water supply |  |  |  | 7.08 |  |  |  |  | 0.24 |  | 
 | For industry |  | 6.02 |  |  |  |  |  |  |  |  | 
 | 1.i.3 Soil water | 12.25 | 0 | 0 | 0 |  |  | 0 | 12.25 | 0 |  | 12.25
 | 1.ii. From others: | 0 | 0 | 0 | 0 |  | 0 | 0 | 0.00 |  |  | 0.00
 | 1.ii.1 Collection of precipitation | 0 | 0 | 0 | 0 |  | 0 | 0 | 0.00 | 0 |  | 
 | 1.ii.2 Abstraction from the sea | 0 | 0 | 0 | 0 |  | 0 | 0 | 0.00 | 0 |  | 
Within the economy | 2. Use of water received from other economic units | 8.65 | 2.23 | 32.32 | 12.30 |  | 9.99 | 2.39 | 67.56 | 7.00 | 0 | 74.55
 | 2.а. Reused water |  |  |  |  |  |  |  |  |  |  | 
 | 2.b. Wastewater to sewerage |  |  |  |  |  |  |  |  |  |  | 
3. Total use of water (=1+2) |  | 20.90 | 8.25 | 96.19 | 85.70 |  | 9.99 | 2.39 | 223.5 | 7.24 | 0 | 230.34
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Physical use table (according to the model in SEEA-Water)

## Slide 21: Advantages of simulating data for filling in the SEEA-Water tables
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
        Allows simulation and computation of missing data and/or to check credibility of excising data.
        Allows automations of the process of filling in the tables. In this way the room for errors is reduced significantly.

## Slide 22: Optimization
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Price
Area of possible solutions
Efficiency
т.С
т.А
PF
т.В
PF- Pareto front
т.А- non-dominant point
т. В- dominant point
т.С- unexciting point
Multi objective optimization– there is no single solution
Evolutionary algorithms are using
The principal of evolution – reduced computation time
Very good balance between the use of best solutions and the search of space
Create multiple solutions at each computational step
Front Pareto in multi objective optimization

## Slide 23: Indicative curves
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Type of water use | Used water
 | m3/year
Public water supply | 19 394 283
Agriculture | 8 651 636
Industry | 2 231 000
HPP | 147 071 938
The group of measures aim to reduce:
physical losses by the water networks;
inefficient water use by end users.
Presents the relationship between the effect of certain measure and investment.
Different approach is used to develop the individual curves and shown in next slides.
During the development of RBMPs forecast for water demand can be used.
The development of the indicative curve should be done at lower scale- business plans by water operators, industry, municipalities etc.

## Slide 24: Reducing physical leakages in Pleven
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Steps:
1st – Pressure management
2nd – Active leakage control– in 4 steps
3rd – Replace part of the network
Chart: Investment in million lv
| 0 | 280000 | 543250 | 561250 | 579250 | 597250 | 28226620
 | 0 | 0.1 | 0.37 | 0.54325 | 0.6535 | 0.72296 | 0.82
Measure | Physical leakages reduction on annual basis | Physical losses | Cumulative reduction in losses on an annual basis | Effect on leakage reduction | Investment | Cumulative price
 | m3/year | m3/year | m3/year | % | lv/measure | lv
BAU |  | 4,950,902 |  |  |  | 
Step 1: Pressure management | 495,090 | 4,455,812 | 495,090 | 10% | 280,000 | 280,000
Step 2.1 | 1,336,743 | 3,119,068 | 1,831,834 | 37% | 263,250 | 543,250
Step 2.2 | 2,194,487 | 2,261,324 | 2,689,577 | 54% | 281,250 | 561,250
Step 2.3 | 2,740,324 | 1,715,487 | 3,235,414 | 65% | 299,250 | 579,250
Step 2.4 | 3,084,201 | 1,371,610 | 3,579,292 | 72% | 317,250 | 597,250
Step 3. Network replacing | 1,371,400 |  | 4,950,691 | 82% | 27,349,370 | 28,226,620
Parameters of the complex indicative curve for reducing water losses in the town of Pleven

## Slide 25: Improve water use efficiency in Pleven
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Индикативни криви
Measure | No change of level of comfort |  | Price per capita
 | l/cap/day | % of reduction | lv
Business as usual | 150 | 0 | 0
1st level of retrofit – water fixtures | 120 | 20% | 30-70
2nd level of retrofit- best sanitary appliances and water appliances | 90 | 40% | 200-600
Water reuse- not applied | 75 | 50% | 2400-4000
Reduction of daily water use [Sh., et al., 2009]
Single indicative curves for water use reduction in the town of Pleven
Chart: Investment in millions lv
| 0 | 624240 | 1248345 | 1872585 | 2496690 | 3120930 | 3745035 | 4369275 | 4993380 | 5617620 | 6241725
1st level of retrofit | -3.1411e-06 | 0.020114 | 0.040227 | 0.060344 | 0.080457 | 0.10057 | 0.12069 | 0.14081 | 0.16092 | 0.18104 | 0.20115
2nd level of retrofit | -3.1411e-06 | 0.040088 | 0.08017 | 0.12026 | 0.16034 | 0.20043 | 0.24052 | 0.28061 | 0.32069 | 0.36078 | 0.40086
Only 2nd level of retrofit | -3.1411e-06 | 0.020114 | 0.040227 | 0.060344 | 0.080457 | 0.10057 | 0.12069 | 0.14081 | 0.16092 | 0.18104 | 0.20115

## Slide 26: Improve water use efficiency in Pleven
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Chart: Investment in millions lv
Complex indicative curve for water use reduction in the town of Pleven (results from optimization by Matlab)
Computational scheme for the development of complex indicative curve for water use reduction in the town of Pleven
2 measures – split the population in 2 groups (H1 и H2). And apply the measure (2) for each group. Total of 6 variables
H1
FLR1
SLR1
H2
FLR2
SLR2

## Slide 27: Improve irrigation efficiency
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Type of crops | N | Drip | Sprinkler | Furrow | Sum | Percent of totally irrigated areas
 |  | % | % | % | % | 
Vegetables/ strawberries | 1 | 0.9 | 90.9 | 8.2 | 100 | 67.9
Maize/ sunflower | 2 | 0.0 | 22.3 | 77.7 | 100 | 14.9
Melon | 3 | 0.4 | 69.3 | 30.3 | 100 | 13.3
Fruits | 4 | 55.6 | 0.0 | 44.4 | 100 | 0.3
Tabaco |  | 0.0 | 0.0 | 100.0 | 100 | 3.6
 |  |  |  |  | Σ | 100.0
Percentage distribution of irrigation crops by type of irrigation system for 2009 (according to data by Irrigation company)
Type of crops | Площи |  |  |  | Coefficient of efficiency |  |  | 
 | Drip | Sprinkler | Furrow | Sum |  |  |  | 
 | ha | ha | ha | ha | Drip | Sprinkler | Furrow | Weighted average
Vegetables/ strawberries | 1.1 | 117.6 | 10.643 | 129.34 | 0.94 | 0.79 | 0.65 | 0.780
Maize/ sunflower | 0 | 6.3 | 21.995 | 28.295 | 0.94 | 0.79 | 0.65 | 0.681
Melon | 0.1 | 17.575 | 7.7 | 25.375 | 0.94 | 0.79 | 0.65 | 0.748
Fruits | 0.3 | 0 | 0.24 | 0.54 | 0.94 | 0.79 | 0.65 | 0.811
Tabaco | 0 | 0 | 6.8 | 6.8 | 0.94 | 0.79 | 0.65 | 0.650
 |  |  | Σ | 190.35 |  | Weighted average = |  | 0.756

## Slide 28: Improving irrigation efficiency
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
To reduce water demand
Improving irrigation efficiency
Reducing effectively irrigated area
Minimal investment
Each arrow represents variables in the optimization process
Computation scheme for developing indicative curve for improving irrigation efficiency
The results are Z1 – Z12, representing areas of different crops and irrigation type
Objectives:

## Slide 29: Improving irrigation efficiency
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Chart: Investment in thousands lv
Chart: Effectively irrigated area
Indicative curve for improving irrigation efficiency (results from optimization in Matlab)
Relationship between coefficient of efficiency and effectively irrigated area (results from optimization in Matlab)

## Slide 30: Simultaneous calculations in WEAP and Matlab
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Applying measures
Exporting results from WEAP
Computation of objective function
Stopping criteria
Satisfied?
Generating new sets of values for variables in Toolbox (MATLAB)
Variables
Yes
No
Legend
Pareto front
MATLAB
WEAP21
External files

## Slide 31
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Start
Initial population
Evaluation of individuals
Selection
Crossover and Mutation
Generating new population
Stopping criterion
Result (Pareto Front)
Yes
No
Evaluation of individuals
Optimization process in Matlab
Variables- external files
Applying the measures in WEAP
Exporting the results from WEAP to external files
Chart: 
| 216.27895999999998 | 216.297843 | 216.38238000000243 | 216.46839300000067 | 216.48896400000001 | 216.582761 | 216.582761 | 216.63951299999755 | 216.69542200000001 | 216.82065700000001 | 216.82220300000191 | 216.95033400000167 | 217.22469099999998 | 217.410788 | 217.41147800000007 | 217.48492800000147 | 217.69865999999999 | 217.88869600000231 | 218.15040000000027 | 218.246218 | 218.498651 | 218.59320399999999 | 218.75118700000004 | 219.13959799999998 | 221.86773400000001 | 225.861594 | 231.037578 | 246.47078499999998 | 257.33209699999969 | 257.33209699999969
 | 25030413.7636 | 25025667.0114 | 23556142.7356 | 22442983.575 | 21934583.0978 | 20848307.4075 | 20848307.4075 | 19832849.0737 | 18873636.1412 | 18376173.5312 | 17015443.5844 | 15437322.7705 | 13851269.1048 | 13180575.9123 | 12064084.5324 | 11512101.1657 | 10352671.6723 | 9112280.4523 | 7476621.935 | 6601612.8388 | 5622869.5688 | 4506498.6366 | 3538196.7379 | 2345572.0891 | 1490744.4943 | 920884.0334 | 635350.3858 | 203870.24 | 2247.969 | 2247.969
Result
Script in Matlab
WEAP - Effect
Chart: 
| 0 | 280000 | 543250 | 561250 | 579250 | 597250 | 28226620
 | 0 | 0.1 | 0.37 | 0.54325 | 0.6535 | 0.72296 | 0.82
Chart: 
Chart: 
Chart: 
| 0 | 669000
 | 0 | 0.3
Indicative curves

## Slide 32: Optimization results for 2009
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Chart: Abstracted water [mill.m3/year.]
| 143.70950199999899 | 141.73910699999999 | 138.20409899999999 | 135.251743 | 133.570716 | 129.347825 | 125.12178099999954 | 118.74476500000046 | 118.74476500000046 | 114.183279 | 111.32327699999998 | 108.905325 | 107.03073999999998 | 103.72627900000002 | 100.00780899999998 | 98.412251999999995 | 94.171554999999998 | 91.285637999999949 | 90.664558 | 90.628536999999298 | 90.497890999999996 | 90.373207999999948 | 90.28207399999998 | 90.223692999999983 | 90.192915999999983 | 90.15128799999998 | 90.095326999999983 | 90.043377999999919 | 90.033794999999998 | 89.908934000000002 | 89.881732999999485 | 89.716918000000007 | 89.713836000000001 | 89.653276999999989 | 89.562393999999998 | 89.509215000000026 | 89.485354000000001 | 89.467753000000499 | 89.408953999999994 | 89.362569999999991 | 89.315359000000001 | 89.266498999999982 | 89.253393000000003 | 89.187353000000002 | 89.10262299999998 | 89.057615999999996 | 89.037457000000003 | 88.993547000000007 | 88.945195999999996 | 88.890524999999997 | 88.797233000000574 | 88.758752999999658 | 88.696883 | 88.649274000000005 | 88.615347999999486 | 88.573346999999558 | 88.494139000000587 | 88.460766000000007 | 88.431923000000779
 | 0 | 17831.1723 | 45425.0154 | 67850.9775 | 86524.7867 | 140432.8179 | 168031.247 | 262457.4321 | 262457.4321 | 469101.8907 | 533257.4573 | 642846.3724 | 921659.2075 | 1067491.9245 | 1280487.2316 | 1406063.9423 | 1702667.7023 | 4145586.9683 | 6865341.5907 | 7503094.902 | 9263680.8576 | 10630879.8764 | 11901346.7558 | 14043066.6831 | 15358258.6624 | 16994069.7571 | 20154933.7056 | 21641222.5463 | 23784385.0642 | 26485486.0164 | 28776703.8813 | 34316860.9757 | 36169212.2203 | 38524677.8643 | 40576533.5235 | 42804047.8176 | 44762531.7205 | 45245308.9901 | 48985598.0415 | 49755425.1818 | 51882728.0846 | 54268168.3375 | 54807849.4493 | 57777824.2492 | 61587891.8674 | 63682201.3723 | 64392128.3005 | 66516758.3513 | 68567882.2833 | 71571445.5959 | 75123298.8431 | 76777428.3992 | 79666268.8161 | 81776176.8782 | 83501761.1658 | 85394567.9279 | 88711267.4638 | 90175924.8531 | 91687359.9237
Chart: Abstracted water [mill.m3/year.]
| 143.70950199999899 | 143.70950199999899 | 141.73910699999999 | 138.20409899999999 | 135.251743 | 133.570716 | 129.347825 | 125.12178099999954 | 118.74476500000046 | 118.74476500000046 | 114.183279 | 111.32327699999998 | 108.905325 | 107.03073999999998 | 103.72627900000002 | 100.00780899999998 | 98.412251999999995 | 94.171554999999998 | 91.285637999999949 | 90.664558 | 90.628536999999298 | 90.497890999999996 | 90.373207999999948 | 90.28207399999998 | 90.223692999999983 | 90.192915999999983 | 90.15128799999998 | 90.095326999999983 | 90.043377999999919 | 90.033794999999998 | 89.908934000000002 | 89.881732999999485 | 89.716918000000007 | 89.713836000000001 | 89.653276999999989 | 89.562393999999998 | 89.509215000000026 | 89.485354000000001 | 89.467753000000499 | 89.408953999999994 | 89.362569999999991 | 89.315359000000001 | 89.266498999999982 | 89.253393000000003 | 89.187353000000002 | 89.10262299999998 | 89.057615999999996 | 89.037457000000003 | 88.993547000000007 | 88.945195999999996 | 88.890524999999997 | 88.797233000000574 | 88.758752999999658 | 88.696883 | 88.649274000000005 | 88.615347999999486 | 88.573346999999558 | 88.494139000000587 | 88.460766000000007 | 88.431923000000779
x1(UL)min=0;max=82 | 0 | 0 | 0.025333 | 0.049467 | 0.07037 | 0.12019 | 0.073916 | 0.42378 | 0.41202 | 0.41202 | 2.4141 | 1.0028 | 3.2029 | 13.2538 | 19.986 | 28.9856 | 35.0289 | 57.2963 | 72.1975 | 71.6186 | 72.2363 | 72.3367 | 72.8424 | 72.7583 | 72.3633 | 72.8434 | 73.8835 | 75.2591 | 73.4888 | 76.5817 | 75.513 | 76.0789 | 78.1063 | 77.3326 | 77.8521 | 79.6794 | 80.793 | 78.3447 | 80.0261 | 78.0787 | 79.8177 | 79.8448 | 81.2418 | 80.0213 | 79.8343 | 81.4106 | 80.5717 | 80.8396 | 80.1765 | 81.2073 | 79.8547 | 81.0345 | 81.4325 | 81.2587 | 81.4821 | 81.0687 | 81.2342 | 81.873 | 81.9811 | 82
x2(UD)min=0;max=40 | 0 | 0 | 0.0077632 | 0.0067829 | 0.0021181 | 0.0035583 | 0.0047019 | 0.0054934 | 0.014491 | 0.014491 | 0.040366 | 0.016541 | 0.017126 | 0.084033 | 0.057974 | 0.13913 | 0.19048 | 0.55598 | 6.2124 | 16.6584 | 16.5763 | 19.5392 | 19.4942 | 20.4181 | 21.8369 | 21.8329 | 21.3738 | 21.0693 | 23.4528 | 21.0493 | 23.1804 | 23.4457 | 23.4235 | 24.8378 | 25.1947 | 24.1255 | 23.822 | 26.9503 | 25.4378 | 28.671 | 27.2576 | 27.9869 | 27.4804 | 28.8693 | 30.1241 | 29.9155 | 31.4944 | 31.4819 | 32.8975 | 32.6194 | 34.9992 | 35.1225 | 35.3112 | 36.5204 | 37.0504 | 38.0727 | 38.5669 | 39.1386 | 39.554 | 39.9996
x3(AL)min=0;max=30 | 0 | 0 | 0.040105 | 0.12072 | 0.16845 | 0.31173 | 1.5408 | 0.20753 | 1.844 | 1.844 | 8.1848 | 13.4021 | 14.6805 | 15.6825 | 17.4233 | 18.116 | 20.2219 | 25.0048 | 29.668 | 29.8081 | 29.7107 | 29.544 | 29.9029 | 29.9522 | 29.9423 | 29.9586 | 29.9631 | 29.8818 | 29.9669 | 29.8438 | 29.9923 | 29.9364 | 29.9956 | 29.9194 | 29.9184 | 29.9988 | 29.9937 | 29.9925 | 29.9958 | 29.9675 | 29.9962 | 29.9978 | 29.9468 | 29.9983 | 29.9981 | 29.9633 | 29.9876 | 29.9907 | 29.9951 | 29.9831 | 29.9926 | 29.9993 | 29.9986 | 29.9967 | 29.9993 | 29.9954 | 29.9958 | 29.9985 | 29.9998 | 29.9999
x4(AD)min=75.63;max=92.96 | 75.63 | 75.63 | 76.3412 | 77.6591 | 78.8334 | 79.5164 | 80.9923 | 83.4381 | 86.1395 | 86.1395 | 86.2195 | 85.964 | 86.8614 | 87.3439 | 88.9945 | 91.6797 | 91.8005 | 92.8668 | 92.937 | 92.8895 | 92.9528 | 92.9445 | 92.8977 | 92.9505 | 92.9549 | 92.9393 | 92.9325 | 92.9457 | 92.947 | 92.9123 | 92.9563 | 92.9353 | 92.952 | 92.94 | 92.9474 | 92.958 | 92.9513 | 92.9533 | 92.9402 | 92.9482 | 92.9575 | 92.9582 | 92.9588 | 92.9494 | 92.9543 | 92.9555 | 92.9516 | 92.9544 | 92.9578 | 92.955 | 92.9522 | 92.9586 | 92.9582 | 92.9589 | 92.9575 | 92.9599 | 92.96 | 92.9593 | 92.9596 | 92.96
Pareto Front for Vit river sub-basin for 2009 (results from optimization in Matlab)
Relationship between values of the optimization variables (measures) and abstracted water for 2009 (results from optimization in Matlab)
Population size of 60. Results after 102 generations and computational time of 15 hours.

## Slide 33: Optimization results for 2011
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Chart: Abstracted water [mill.m3/year.]
| 151.02406499999998 | 147.79410499999992 | 145.39595800000001 | 141.00377099999992 | 136.29764700000001 | 128.84289700000087 | 120.96744400000046 | 118.248831 | 115.618469 | 110.65676099999995 | 107.11913699999998 | 103.789557 | 102.17787899999924 | 98.951603000000574 | 95.721864999999994 | 95.649125000000026 | 92.833106000000001 | 91.986729999999994 | 91.719943000000427 | 91.106570999999988 | 91.053351999999919 | 91.051513999999997 | 90.955829999999992 | 90.913021000000327 | 90.881365000000002 | 90.818070999999989 | 90.769733000000002 | 90.734815999999995 | 90.697775999999948 | 90.683531999999758 | 90.628053999999949 | 90.599514000000127 | 90.570840999999959 | 90.517893000000427 | 90.451374999999999 | 90.393552999999983 | 90.370467999999988 | 90.332164000000006 | 90.261506999999995 | 90.201747999999981 | 90.170461999999958 | 90.082316999999989 | 90.038332999999326 | 89.970420000000004 | 89.932021000000006 | 89.836920000000006 | 89.816860000000005 | 89.800806999999978 | 89.730728999999982 | 89.680721999999989 | 89.624482999999515 | 89.571850999999981 | 89.491634000000545 | 89.461498000000006 | 89.425227000000007 | 89.369105000000005 | 89.309635 | 89.305160999999998 | 89.305160999999998
 | 0 | 30077.8059 | 50368.7615 | 50682.207 | 98043.7289 | 132327.3208 | 174561.3759 | 187057.607 | 221265.024 | 304078.798 | 494163.8354 | 752997.9897 | 890443.4593 | 1512548.8507 | 1995838.3055 | 2623837.0244 | 3463083.6246 | 5669341.107 | 9195272.3954 | 10371837.8954 | 11868390.9972 | 13849179.2038 | 15319725.4902 | 17680431.5443 | 18838553.1542 | 21505968.3299 | 22984184.3411 | 24345987.5663 | 26199790.6361 | 27089316.7578 | 29343841.9079 | 31642024.8509 | 31874552.6638 | 35011295.6859 | 37574462.0355 | 39984216.0584 | 41095654.3721 | 44477415.7439 | 46191151.3971 | 49085513.9826 | 50382392.3398 | 55631504.5596 | 58017773.1462 | 60500502.7634 | 61942167.7207 | 65839413.5455 | 67014201.8484 | 68915213.2439 | 71206232.5156 | 73876231.7532 | 76295938.2852 | 79196172.8753 | 83127338.0242 | 84317984.7689 | 86467180.2009 | 88781084.9708 | 91273348.3905 | 91699904.6672 | 91699904.6672
Pareto Front for Vit river sub-basin for 2011 (results from optimization in Matlab)
Chart: Abstracted water [mill.m3/year.]
| 151.02406499999998 | 151.02406499999998 | 147.79410499999992 | 145.39595800000001 | 141.00377099999992 | 136.29764700000001 | 128.84289700000087 | 120.96744400000082 | 118.248831 | 115.618469 | 110.65676099999995 | 107.11913699999998 | 103.789557 | 102.17787899999804 | 98.951603000001327 | 95.721864999999994 | 95.649125000000026 | 92.833106000000001 | 91.986729999999994 | 91.719943000000427 | 91.106570999999988 | 91.053351999999919 | 91.051513999999997 | 90.955829999999992 | 90.913021000000327 | 90.881365000000002 | 90.818070999999989 | 90.769733000000002 | 90.734815999999995 | 90.697775999999948 | 90.683531999999758 | 90.628053999999949 | 90.599514000000127 | 90.570840999999959 | 90.517893000000427 | 90.451374999999999 | 90.393552999999983 | 90.370467999999988 | 90.332164000000006 | 90.261506999999995 | 90.201747999999981 | 90.170461999999958 | 90.082316999999989 | 90.038332999998858 | 89.970420000000004 | 89.932021000000006 | 89.836920000000006 | 89.816860000000005 | 89.800806999999978 | 89.730728999999982 | 89.680721999999989 | 89.624482999999458 | 89.571850999999981 | 89.491634000001127 | 89.461498000000006 | 89.425227000000007 | 89.369105000000005 | 89.309635 | 89.305160999999998 | 89.305160999999998
x1(UL)min=0;max=82 | 0 | 0 | 0.097392 | 0.021653 | 0.0080471 | 0.025367 | 0.066699 | 0.027629 | 0.010004 | 0.035278 | 0.21844 | 0.24599 | 0.38881 | 0.46182 | 22.7798 | 52.1064 | 62.1029 | 68.9828 | 72.9981 | 73.8634 | 72.7088 | 72.9752 | 73.5345 | 73.003 | 72.9565 | 75.2403 | 76.3741 | 76.1489 | 76.3759 | 76.7768 | 76.2753 | 78.4257 | 77.1506 | 78.0758 | 78.0276 | 78.2793 | 79.2176 | 79.5688 | 76.4931 | 81.0207 | 79.3358 | 80.2313 | 81.2288 | 78.3737 | 79.4134 | 80.4395 | 81.6885 | 81.3064 | 80.0419 | 81.5123 | 80.9493 | 81.6708 | 81.4869 | 80.8451 | 81.1473 | 80.7755 | 81.2047 | 81.9707 | 82 | 82
x2(UD)min=0;max=40 | 0 | 0 | 0.0068803 | 0.042798 | 0.00027383 | 0.060786 | 0.057634 | 0.0086426 | 0.0014838 | 0.01148 | 0.0094149 | 0.057405 | 0.049644 | 0.010634 | 0.7635 | 1.6292 | 3.4814 | 5.8866 | 3.9742 | 7.6204 | 19.6263 | 20.082 | 20.2777 | 21.6788 | 22.5881 | 20.4469 | 20.1918 | 21.2561 | 21.5918 | 21.8229 | 22.6872 | 21.2863 | 23.412 | 22.6062 | 23.7813 | 24.4173 | 24.3529 | 24.4027 | 28.6016 | 24.6637 | 27.5162 | 27.0864 | 27.9603 | 31.6472 | 31.5019 | 31.0115 | 31.1648 | 31.9643 | 33.8871 | 33.2568 | 34.7587 | 34.8988 | 36.1244 | 38.1609 | 38.2875 | 39.4195 | 39.821 | 39.9554 | 39.9998 | 39.9998
x3(AL)min=0;max=30 | 0 | 0 | 0.47053 | 0.4419 | 0.0014903 | 0.1135 | 0.03023 | 0.49658 | 0.25668 | 0.71238 | 0.96859 | 7.4593 | 18.8889 | 25.4803 | 21.9916 | 23.9559 | 22.6801 | 28.6309 | 29.9743 | 29.9526 | 29.9436 | 29.9638 | 29.8989 | 29.9889 | 29.9801 | 29.9901 | 29.9948 | 29.9967 | 29.9967 | 29.9916 | 29.9803 | 29.98 | 29.9295 | 29.9927 | 29.9653 | 29.9926 | 29.9929 | 29.9867 | 29.9793 | 29.9808 | 29.9949 | 29.9919 | 29.9964 | 29.9808 | 29.9961 | 29.9845 | 29.999 | 29.9941 | 29.9793 | 29.987 | 29.9981 | 29.9913 | 29.9679 | 29.9915 | 29.9983 | 29.9853 | 29.9983 | 29.9999 | 29.9999 | 29.9999
x4(AD)min=75.63;max=92.96 | 75.63 | 75.63 | 76.3851 | 77.0031 | 78.2494 | 79.564 | 81.4557 | 83.9665 | 84.9999 | 85.9388 | 88.6756 | 89.6166 | 89.6936 | 89.7168 | 92.0597 | 92.5495 | 92.3451 | 92.7354 | 92.9529 | 92.9567 | 92.9546 | 92.9574 | 92.9393 | 92.955 | 92.9524 | 92.9557 | 92.9582 | 92.9585 | 92.959 | 92.9583 | 92.9586 | 92.9568 | 92.9578 | 92.9568 | 92.9541 | 92.9579 | 92.9588 | 92.9578 | 92.9555 | 92.9589 | 92.959 | 92.9583 | 92.9401 | 92.9529 | 92.9563 | 92.9586 | 92.9598 | 92.9594 | 92.9538 | 92.9598 | 92.9572 | 92.9599 | 92.9596 | 92.9581 | 92.9591 | 92.9582 | 92.9592 | 92.9599 | 92.9599 | 92.9599
Relationship between values of the optimization variables (measures) and abstracted water for 2009 (results from optimization in Matlab)
Population size of 60. Results after 102 generations and computational time of 15 hours.

## Slide 34: Scenarios
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Climate change- increase in evapotranspiration and reduction in precipitation
Economic – increase in irrigated areas
Combined- moderate combination between climate change and economic scenarios
  10% reduction in precipitation
  10% increase in evapotranspiration
  Increase in irrigated areas 10 times
Irrigated areas (designed and current), according to data by Irrigation company
Chart: 
| Designed irrigated areas | Irrigated areas in 2009
 | 711000 | 18750

## Slide 35: Combined scenarios
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Unmet demand for Vit river sub-basin
The unmet demand occur for water user supplied by Gorni dabnik and Dolni dabnik reservoirs. These are irrigated fields and indrustrial areas in the towns of Pleven and Dolna mitropolia.
Simulated abstracted water is 487 mill.m3/year
Compare with 143 mill.m3/year in the reference 2009

## Slide 36: Optimization results for combined scenario
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders
Chart: Abstracted water [mill.m3/year.]
| 487.23043899999863 | 476.246985 | 462.05867000000001 | 460.62083699999999 | 447.91103299999384 | 434.02787899999993 | 417.66791599999999 | 398.89768299999997 | 396.518621 | 381.51788800000008 | 362.22980799999999 | 351.584586 | 334.71976000000001 | 308.65197499999999 | 299.25260600000001 | 285.47783699999923 | 273.019497 | 259.13869299999999 | 237.74602899999999 | 217.21417899999992 | 214.71360299999569 | 192.101225 | 177.06027599999999 | 173.42250900000047 | 156.495541 | 145.08058800000001 | 128.24735299999998 | 122.13889399999998 | 116.831931 | 116.45559299999998 | 116.45553200000001 | 116.29798000000002 | 116.22752100000002 | 116.14128700000002 | 116.03446400000072 | 115.94328899999999 | 115.89558799999998 | 115.82537699999835 | 115.724456 | 115.67899499999965 | 115.630667 | 115.519238 | 115.44756900000219 | 115.366321 | 115.27451499999999 | 115.20946300000062 | 115.155215 | 115.12084299999873 | 115.070809 | 115.06990999999999 | 114.99291400000052 | 114.92052000000002 | 114.83633799999915 | 114.751991 | 114.65379199999883 | 114.60647499999995 | 114.563361 | 114.50737599999998 | 114.50737599999998
 | 0 | 262406.6187 | 583763.8526 | 614473.1151 | 812215.8425 | 1034030.5951 | 1339300.9595 | 1543475.8701 | 1574877.7838 | 1677264.8841 | 1713404.2873 | 1790352.253 | 1859321.1498 | 2009092.5305 | 2064589.644 | 2146404.9617 | 2200195.6588 | 2313703.866 | 2514267.0818 | 2830561.3694 | 2897551.4649 | 3558557.6689 | 3888435.8378 | 3929449.1013 | 4321837.0084 | 4384781.5659 | 4793574.8935 | 6515612.4869 | 10450426.1747 | 14075408.6937 | 14075744.2311 | 17664106.8849 | 20299100.7429 | 23438475.4838 | 28408351.1583 | 31327262.7608 | 33477787.2089 | 36309595.3519 | 39955816.5578 | 42655405.1906 | 44037283.9368 | 49834068.9941 | 53914812.352 | 56471940.6232 | 61304521.2051 | 63666925.9481 | 66795396.5903 | 67575491.7879 | 70266659.4114 | 70568219.5296 | 73394622.7005 | 77295523.3748 | 81053169.3376 | 84284599.7207 | 88673221.845 | 91610806.7957 | 92924797.4556 | 95353636.3231 | 95353636.3231
Pareto Front for Vit river sub-basin for combined scenario (results from optimization in Matlab)
Chart: Abstracted water [mill.m3/year.]
| 487.23043899999863 | 487.23043899999863 | 476.246985 | 462.05867000000001 | 460.62083699999999 | 447.91103299999384 | 434.02787899999993 | 417.66791599999999 | 398.89768299999997 | 396.518621 | 381.51788800000008 | 362.22980799999999 | 351.584586 | 334.71976000000001 | 308.65197499999999 | 299.25260600000001 | 285.47783699999923 | 273.019497 | 259.13869299999999 | 237.74602899999999 | 217.21417899999992 | 214.71360299999569 | 192.101225 | 177.06027599999999 | 173.42250900000047 | 156.495541 | 145.08058800000001 | 128.24735299999998 | 122.13889399999998 | 116.831931 | 116.45559299999998 | 116.45553200000001 | 116.29798000000002 | 116.22752100000002 | 116.14128700000002 | 116.03446400000072 | 115.94328899999999 | 115.89558799999998 | 115.82537699999835 | 115.724456 | 115.67899499999965 | 115.630667 | 115.519238 | 115.44756900000219 | 115.366321 | 115.27451499999999 | 115.20946300000062 | 115.155215 | 115.12084299999873 | 115.070809 | 115.06990999999999 | 114.99291400000052 | 114.92052000000002 | 114.83633799999915 | 114.751991 | 114.65379199999883 | 114.60647499999995 | 114.563361 | 114.50737599999998 | 114.50737599999998
x1(UL)min=0;max=82 | 0 | 0 | 0.0062162 | 0.023048 | 0.42317 | 0.030882 | 0.32608 | 0.42702 | 0.34226 | 0.44445 | 0.30973 | 0.093138 | 0.062712 | 0.3316 | 0.28705 | 0.95838 | 0.57015 | 0.30332 | 0.23009 | 0.75187 | 0.42274 | 0.53077 | 3.7888 | 2.6682 | 3.435 | 2.7624 | 4.453 | 1.4824 | 30.8721 | 71.585 | 72.9423 | 72.9423 | 73.6146 | 74.4869 | 75.0289 | 77.241 | 77.4997 | 78.3223 | 79.0067 | 80.5972 | 81.5912 | 80.8594 | 81.6475 | 80.0573 | 80.4914 | 80.2789 | 81.53 | 80.6578 | 81.8158 | 80.9314 | 80.1388 | 80.9813 | 80.7914 | 81.011 | 81.2458 | 81.4992 | 80.9763 | 81.3065 | 81.9999 | 81.9999
x2(UD)min=0;max=40 | 0 | 0 | 0.0041746 | 4.4334e-05 | 0.00035169 | 0.01189 | 0.0051879 | 0.013443 | 0.010853 | 0.0019994 | 0.11883 | 0.00026296 | 0.072594 | 0.01522 | 0.025585 | 0.013119 | 0.074528 | 0.040879 | 0.13117 | 0.0033034 | 0.016039 | 0.022177 | 0.46252 | 0.64883 | 0.56524 | 0.76099 | 0.34963 | 0.33079 | 4.3072 | 16.2557 | 18.9782 | 18.9792 | 20.2399 | 20.3981 | 21.2012 | 20.6439 | 21.6514 | 21.6152 | 21.9468 | 21.6722 | 21.6585 | 22.9129 | 24.1723 | 27.1942 | 27.6964 | 29.6311 | 29.2359 | 31.2066 | 30.3567 | 32.1855 | 33.0648 | 33.2494 | 34.8197 | 35.9344 | 36.8687 | 38.1837 | 39.7438 | 39.8882 | 39.9995 | 39.9995
x3(AL)min=0;max=30 | 0 | 0 | 0.62802 | 0.12422 | 0.15728 | 0.15058 | 0.76545 | 1.1143 | 0.83408 | 0.61337 | 0.40805 | 0.5566 | 0.16528 | 0.65148 | 0.80161 | 2.4447 | 0.80973 | 0.13546 | 0.77391 | 2.1563 | 0.88079 | 0.94367 | 12.0859 | 18.1031 | 12.3045 | 16.8705 | 9.2439 | 29.9943 | 27.8256 | 29.9863 | 29.9399 | 29.9399 | 29.9852 | 29.9866 | 29.9867 | 29.9851 | 29.9891 | 29.9955 | 29.9821 | 29.9978 | 29.9765 | 29.9976 | 29.9801 | 29.992 | 29.9941 | 29.9905 | 29.9964 | 29.9849 | 29.9969 | 29.9946 | 29.9982 | 29.995 | 29.993 | 29.9954 | 29.997 | 29.9981 | 29.9941 | 29.9967 | 29.9995 | 29.9995
x4(AD)min=75.63;max=92.96 | 75.63 | 75.63 | 76.9081 | 78.6445 | 78.7524 | 79.8083 | 80.8895 | 82.4156 | 83.5212 | 83.7027 | 84.0845 | 84.5007 | 84.7924 | 85.1518 | 85.8053 | 85.8867 | 86.3568 | 86.7264 | 87.0568 | 87.7326 | 88.8732 | 89.0448 | 89.6423 | 90.1852 | 90.7382 | 91.5225 | 92.5178 | 92.6294 | 92.9179 | 92.9517 | 92.9596 | 92.9596 | 92.9599 | 92.9599 | 92.96 | 92.9598 | 92.96 | 92.9599 | 92.9599 | 92.96 | 92.9596 | 92.96 | 92.9596 | 92.9593 | 92.9599 | 92.9598 | 92.9596 | 92.9594 | 92.9598 | 92.9599 | 92.9599 | 92.96 | 92.9598 | 92.9598 | 92.96 | 92.96 | 92.9599 | 92.96 | 92.96 | 92.96
Relationship between values of the optimization variables (measures) and abstracted water for combined scenario (results from optimization in Matlab)

## Slide 37
THANK YOU FOR YOUR ATTENTION!
Strengthening of master curricula in water resources management
for the Western Balkans HEIs and stakeholders